## Slide 1: Computed Tomography at LLNL
Kyle Champley
PI in the Nondestructive Characterization Institute (NCI)
Signal and Imaging Processing Research Group Leader
Director of the Center for Advanced Signal & Imaging Sciences (CASIS)

## Slide 2
B.S. Mathematics/ Computer Science
Western Washington University
1997 - 2001

## Slide 3
M.S. Mathematics
Oregon State University
Thesis
SPECT Reconstruction Using the Expectation Maximization Algorithm and an Exact Inversion Formula
2002 - 2006

## Slide 4
Ph.D. Electrical Engineering
University of Washington
Real-Time analytic PET reconstruction for box geometries
Bayesian estimation method for depth of interaction estimation in PET detector
Dissertation
Algorithms for High-Resolution Positron Emission Tomography
2006 - 2010

## Slide 5
CT Imaging Scientist
GE Global Research
Developed reconstruction algorithms for the GE Revolution CT system (wide cone 256-slice system)
Developed reconstruction algorithms for ultrasonic guided-wave system for monitoring pipe corrosion
2010 - 2012

## Slide 6
Staff Scientist & Group Leader
Lawrence Livermore National Lab
Specializing in quantitative CT and sparse/ few-view CT reconstruction methods
Independent Contractor
Imatrex, Inc (EB-CT)
PET/X (Mammography/ PET)
Precision Sensing (SPECT)
2012 - present

## Slide 7: LLNL is a Federally Funded National Laboratory Specializing in National Security
Primary Customers
Nuclear Weapons Program
  components must be inspected with NDE techniques
  insensitive high explosives
Advanced Manufacturing (3D Printing)
  metals and polymers
National Ignition Facility (NIF) and Photon Science
  inspection is deuterium/tritium targets
Border and Aviation Security
  R&D and testing/evaluation of scanners at seaports and airports
Nonproliferation and Treaty Verification

## Slide 9: We desired a tomographic software toolkit capable of processing CT data for such diverse needs with exceptional quantitative accuracy… so we developed Livermore Tomography Tools

## Slide 10
can process CT data from any scanner geometry
on a computer running any OS
parallel
fan
cone
custom
and any GPU/accelerator hardware vendor
with rapid processing and exceptional accuracy
(in specified units) using state of the art algorithms

## Slide 11: Quantitative CT
Scatter Correction
Multi-material Beam Hardening Correction
Reconstruction
Gain Correction
raw CT data
Detector Deblur
x-ray cross sections
x-ray spectrum
x-ray spectrum
detector PSF
x-ray scatter distributions
Detector Response versus Flux

## Slide 12: Physics-based algorithms remove beam hardening, scatter, and other effect that diminish quantitative accuracy and introduce artifacts
Red arrows point to artifacts
Green arrows point to true voids
Without physics-based algorithms, it is not possible to distinguish between artifacts and true features!
Standard Reconstruction
Physics-Based Reconstruction
CT slice of Metal AM Lattice

## Slide 13
Metal streaks/ shading artifacts make it difficult to recover conductive traces in PBCs
Standard Processing (FBP)

## Slide 14: Physics-Based Correction Algorithms and Iterative Reconstruction
Physics-based iterative reconstruction algorithms in LTT provide best-in-class image quality

## Slide 15: System Independent Rho-e/ Ze (SIRZ) (Electron Density/ Effective Atomic Number)
Conventional X-ray Feature Space
Rho-e/ Ze Feature Space
Quantitatively-accurate dual energy decomposition algorithms enabling estimation system independent material features
Champley et al., IEEE TNS, 2019
Used by DHS/TSA, FBI, and UK Home Office to characterize x-ray signatures of homemade explosives

## Slide 16
Metal Artifact Reduction (MAR) for airport luggage CT
Standard Processing
MAR
When luggage contains significant metal, reconstructions are nearly useless without MAR
Joint work with Seemeen Karimi

## Slide 17: Sparse/ Few View CT reconstructing with 10-100 times fewer projections than conventional CT
Solve using constrained optimization
Distance Metric
Forward Model
Measured Data
Solution Space
Method to constrain solution space
Total Variation
Dictionary of Patches
Histogram Sparsity
Manifold of Solutions from Deep Learning
others

## Slide 18: Reconstruction of armor-penetrating bullet with 5 truncated projections
Collaboration with Michael Zellner at the Army Research Laboratory (ARL)
ARL 15-head flash x-ray
Reconstruction using only the five 300 kV sources

## Slide 19: 7-View Reconstruction of In-Flight (2.5 km/sec) Slapper Initiator
Willey, Champley, Hodgin, Lauderbach, Bagge-Hansen, May, Sanchez, Jensen, Iverson, van Buuren

## Slide 20: Our reconstruction shows good recovery of features from only 15 projections
Reconstruction with 1440 views
Our reconstruction from 15-views with non-convex image priors
only 15 projections of the original 1440 were used in this reconstruction

## Slide 21: Our reconstruction outperforms other state of the art approaches
State-of-the-art reconstruction from 15 views
Our reconstruction from 15-views with non-convex image priors

## Slide 22: 180 μm diameter glass fiber reconstruction with 19 views
State of the Art Method
LTT
the germanium-doped core is only visible with the LTT algorithm

## Slide 23: Thank You!
NCI Website
https://nci.llnl.gov/

## Slide 24: Physics-Based Scatter Correction
detector
response
x-ray flux per unit area
probability of scatter at x
probability no x-ray interaction before x
probability of scattering angle
probability no x-ray interaction from x to detector
integration
time
Model of First Order Scatter
Higher order scatter estimated by Monte-Carlo simulation. Estimate by a single number, so don’t need to simulate very many x-rays.
x
x0
xd
x

## Slide 25: Beam Hardening is Caused by the Preferential Absorption of Low Energy X-rays
Mean Energies:
original spectrum: 45.5 keV
through 10 cm of water: 48.2 keV
through 20 cm of water: 50.2 keV
through 30 cm of water: 51.8 keV
original
10 cm water
20 cm water
30 cm water
measured
data
spectrum
areal
density
effective cross section

## Slide 26: Multi-material Beam Hardening Correction
FBP
water
image
aluminum
image
titanium
image
forward projection
forward projection
forward projection
÷
÷
÷
x
x
x
+
Sinogram Data
Initial Reconstruction
Estimate of cross section for each ray path can be used to remove beam hardening artifacts.

## Slide 27
Dynamic CT of heating a sample (13 views per rotation/ 29 rotations)
initial state
middle state
final state

## Slide 28
Abel Reconstruction
Iterative Reconstruction
Nielsen, Michael H., et al. "Single-bunch imaging of detonation fronts using scattered synchrotron radiation.” Journal of Applied Physics 123.22 (2018): 225902.
Detonation Experiment with DNTF reconstructions with a single projection

## Slide 29
State of the Art Method
LTT
Reconstruction of industrial object with plastic and metal parts from 40 views